## Slide 1: Active Wheelset Steering (AWS)
SD2231
May 3, 2018
A. Qazizadeh

## Slide 2: Two-axle rail vehicle
poor comfort
low hunting speed
limited wheelbase (limiting capacity)
Candidate for a passenger vehicle?
Why?
no bogie poor curving (wear, squeal noise)
limited wheelbase

## Slide 3: Active Wheelset steering
Possible solution:
Active Wheelset Steering
better curving (less wear)
increasing wheelbase (increasing capacity)
Wheelset top view

## Slide 4: controller
is a model based controller equations of the motion for the vehicle.
  Lateral dynamics is enough
  2 bodies, 4 degrees of freedom
Equations are then written in state space form and then implemented in Simulink.
Control strategy: control
Why? Robustness to model variations and good disturbance rejection.

## Slide 5: Controller design: controller
input yaw angle of the wheelset
output torque to be applied by actuators

## Slide 6: concept
norm:
of a transfer function is its maximum magnitude over the whole frequency range.
-
+
r
y
T(s)
control tries to design the controller such that the infinity norm of the closed loop transfer function is minimized.
We can focus this minimization process on specific frequency ranges by proper weighting functions (penalizing)
frequency

## Slide 7: Weighting functions
The control is tuned through selection of weighting functions
related to maximum load
the actuator cut-off frequency
related to desired steady state tracking error
affects the system time constant.
reference yaw angle
radius, cant angle
wheelset yaw
error signal
torque

## Slide 8: Designed Controller
controller has high magnitude at lower frequencies which provides good reference tracking and low magnitude at higher frequencies for better disturbance rejection.

## Slide 9: Actuator force request
Random behaviour
Follows low frequency and disregards high frequencies.
Low frequency content as expected from the physics of the problem.

## Slide 10: Wear number
By increasing wheelbase wear number increases as well.
AWS brings significant reduction in wear number.
wear number [N]
Increasing axle distance by 2 m

## Slide 11: Cut-off frequency:
Cut-off frequency is a boundary in a system’s frequency response at which energy flowing through the system is dropped to half the pass-band power: